Studies of the dynamic range of TileCal cells in high-pT jets
Jordan Dull
St. Olaf College, Northfield, MN
Sergei Chekanov
Argonne National Laboratory, Lemont, IL

---
ATLAS Detector
- Part of ATLAS experiment at the Large Hardon Collider at CERN
- Inner detector, calorimeter, muon spectrometer, magnet system

---
Tile Calorimeter in ATLAS
- TileCal searches for:
  - jet transverse momentum
  - long-lived particles
  - missing energy
  - tau decays
- Plastic scintillator separated by absorbing steel plates
  - Measure up to 1.2 or 1.5 TeV
- A jet is a cone of particles that results from quark and gluon fragmentation

---
Purpose of Research
- Jet energy can be as large as 4 TeV
- Do we have biases in jet reconstruction due to the limited dynamic range of photo-multiplier tubes and electronics in TileCal?
- Using a full ATLAS simulation, calculate energy ranges for TileCal cells
- Use a fast simulation (x100 faster) for further study

---
ATLAS full simulation: Dynamic range of cells
14 TeV, Standard Model events
Dynamic range for 0.1 x 0.1 cells: Layer A and BC
Plot shows fractions of jets (in %) that have at least one cell above 1.2 (1.5) TeV

---
Delphes
- Fast simulation of collider experiment
  - Implements Liquid Argon calorimeter and Tile calorimeter as “towers”
  - TileCal towers have sizes 0.1x0.1
  - Longitudinal cell segmentation needs to be simulated
DELPHES TOWERS

---
Full simulation vs Delphes
14 TeV, Standard Model events
Plots show fractions of jets (in %) that have at least one cell above 1.2 (1.5) TeV
Full simulation and Delphes show similar fractions (but shapes are different)

---
Future Circular Collider (FCC)
- Energy: 100 TeV for proton-proton collisions
- Circumference: 80-100 km
- Necessary detector energy range unknown

---
FCC Detector
Dynamic range of cells for 100 TeV, Standard Model events
Jet pT > 20 TeV
Dynamic range for 0.025x0.025
Dynamic range for 0.1x0.1 cells
x4 reduction of cell sizes helps to reduce dynamic range by a factor of ~1.5

---
Summary
- Energy range of TileCal cells was studied using Standard Model events for LHC and FCC
- Comparable results between Delphes and full simulation
- Effects of dynamic range truncations at 1.2 TeV and 1.5 TeV were quantified
  - Optimistic scenario
- Approximate dynamic range of a FCC calorimeter was obtained

---
Acknowledgments
I would like to thank my mentor, Sergei Chekanov, for guiding me through my research and offering helpful suggestions for its improvement. Further thanks to the whole ATLAS Analysis Support Center for feedback on my research. My gratitude to the U.S Department of Energy-Office of Science Education for supporting internships such as this. Finally, my thanks to Argonne National Laboratory for hosting summer students and allowing us to experience a career in research.
This work was supported in part by the U.S. Department of Energy, Office of Science, Office of Workforce Development for Teachers and Scientists (WDTS) under the Science Undergraduate Laboratory Internships Program (SULI)
Argonne National Laboratory is a U.S. Department of Energy laboratory manage by UChicago Argonne, LLC.

---
References
- K. Brom, S. Chekanov, D. Nguyen, J. Proudfoot, Monte Carlo simulation of high-pT jets in the Tile calorimeter. March 2015.
- J. Proudfoot, Hadron Calorimetry at the LHC, 2006. http://www.slac.stanford.edu/econf/C060717/proceedings.htm.
- L. Heelan and A. Collaboration, Preformance of the ATLAS Tile Calorimeter, March 2015. https://cds.cern.ch/record/2005212.
- Delphes Fast Simulation. https://cp3.irmp.ucl.ac.be/projects/delphes